## Slide 1: TRILL Tutorial Transparent Interconnection of Lots of Links
Donald E. Eastlake 3rd
Co-Chair, TRILL Working Group
Principal Engineer, Huawei
d3e3e3@gmail.com

## Slide 2
Donald E. Eastlake, 3rd
Principal Engineer at Huawei Technologies
  Previously with Cisco Systems and before that with Motorola Laboratories.
Co-Chair of the IETF TRILL Working Group
  Chair of the IETF PPPEXT Working Group
  Chair of the IEEE 802.11ak Task Group
Author of 61 IETF RFCs.
Note:
This tutorial represents my personal views, not those of the TRILL WG or Huawei. It is a high level technical overview. It is not practical to include all the details in the specification documents in a presentation of this length.

## Slide 3: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 4: What is TRILL?
A Compatible Protocol
  Attached end nodes just think it is Ethernet.
The more bridges you convert to TRILL switches, the better your network’s stability and bandwidth utilization.
Terminates Spanning Tree Protocols

## Slide 5: What is TRILL?
Basically a simple idea:
  Encapsulate native frames in a transport header providing a hop count
  Route the encapsulated frames using IS-IS
  Decapsulate native frames before delivery
Provides
  Least cost paths with zero/minimal configuration
  Equal Cost Multi-Pathing of unicast
  Multi-paths of multi-destination

## Slide 6: What is TRILL?
TRansparent Interconnection of Lots of Links
  TRILL WG Charter
    http://www.ietf.org/dyn/wg/charter/trill-charter.html
  Standardized by IETF TRILL Working Group:
    Donald E. Eastlake 3rd (Huawei), Co-Chair
    Erik Nordmark (Cisco), Co-Chair
    Jon Hudson (Brocade), Secretary
TRILL Switch / RBridge (Routing Bridge)
  Device that implements TRILL
TRILL/RBridge Campus –
  A network of RBridges, links, and any intervening bridges, that connects end stations and layer 3 routers.

## Slide 7: A TRILL Campus
End stations and Layer 3 routers are connected to TRILL switches by Ethernet.
TRILL switches can be connected to each other with arbitrary technology.
In both cases, the connection can be a bridged LAN.
= end station
= Ethernet
= Any technology
RB1
RB2
L3 Router
RB3
L3 Router
RB4
RB5
Bridge 2
Bridge 3
Bridge 1
RB6

## Slide 8: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 9: Unicast Least Cost Paths
= end station
B2
B3
B1
A three bridge network

## Slide 10: Unicast Least Cost Paths
Spanning tree eliminates loops by disabling ports
= end station
B2
B3
B1

## Slide 11: Unicast Least Cost Paths
RB2
= end station
RB3
RB1
A three RBridge network: better performance using all facilities

## Slide 12: Unicast Multi-Pathing
B2
= end station
B4
B3
B1
Bridges limit traffic to one path
B5

## Slide 13: Unicast Multi-Pathing
RB2
= end station
RB4
RB3
RB1
RBridges support multi-path for higher throughput
RB5

## Slide 14: Multi-Pathing (Unicast)
= end station
B3
Bridges limit traffic to one path
B2
B4
B1
B5
B6
B7

## Slide 15: Multi-Pathing (Unicast)
RBridges support multi-pathing for higher throughput
RB3
RB2
RB4
RB1
RB5
RB6
RB7
= end station

## Slide 16: Multi-Pathing (Multi-destination)
Spanning tree yields a single bi-directional tree for flooding multi-destination frames limiting bandwidth
B3
B2
B4
B1
B5
B6
B7
= end station

## Slide 17: Multi-Pathing (Multi-destination)
RBridges support multiple distribution trees. The encapsulating RBridge chooses which to use. RB2 can split multi-destination traffic over three trees.
RB3
RB2
RB4
RB1
RB5
RB6
RB7
= end station

## Slide 18: Routing versus Bridging
Routing only sends data out a port when it receives control messages on that port indicating this is safe and routing has a TTL for safety.
  If control messages are not received or not processed, it “fails safe” and does not forward data.
Bridging (Spanning Tree Protocol) forwards data out all ports (except the one where the data was received) unless it receives control messages on that port indicate this is unsafe. There is no TTL.
  If control messages are not received or not processed, it “fails unsafe”, forwards data, and can melt down due to data loops.

## Slide 19: TRILL Features
Bridges
Routers
TRILL Switch
Transparency
Plug & Play
Virtual LANs
  Multi-tenant support
Frame Priorities
Data Center Bridging
Virtualization Support
Multi-pathing
Optimal Paths
Rapid Fail Over
The safety of a TTL
  Implemented in data plane
Extensions

## Slide 20: More TRILL Features
Breaks up and minimizes spanning tree for greater stability.
Unicast forwarding tables at transit RBridges scale with the number of RBridges, not the number of end stations.
Transit RBridges do not learn end station addresses.
Compatible with existing IP Routers. TRILL switches are as transparent to IP routers as bridges are.
Support for VLANs, frame priorities, and 24-bit data labels (“16 million VLANs”).

## Slide 21: More TRILL Features
MTU feature and jumbo frame support including jumbo routing frames.
Has a poem.
  The only other bridging or routing protocol with a poem is Spanning Tree (see Algorhyme).

## Slide 22: Algorhyme V2 (TRILL and RBridges)
I hope that we shall one day see
A graph more lovely than a tree.
A graph to boost efficiency
While still configuration-free.
A network where RBridges can
Route packets to their target LAN.
The paths they find, to our elation,
Are least cost paths to destination!
With packet hop counts we now see,
The network need not be loop-free!
RBridges work transparently,
Without a common spanning tree.
- By Ray Perlner (Radia Perlman’s son)

## Slide 23: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 24: Inspired by a Real Life Incident
In November 2002, Beth Israel Deaconess Hospital in Boston, Massachusetts, had a total network meltdown:
  Their network took four days of heroic efforts to be restored to an operational state! In the mean time the staff was reduced to using paper and pencil.
  Beth Israel Deaconess had grown by acquiring various clinics and just plugged all those bridged networks together.
  The article in Boston’s primary newspaper specifically mentioned “Spanning Tree Protocol” as the problem!
  Radia Perlman, who invented spanning tree over 25 years ago, decided it was time to come up with a better way.

## Slide 25: TRILL History up to 2008
  1964: Packet switching/routing invented by Paul Baran.
  1973: Ethernet invented by Robert Metcalfe
  1979: Link State Routing invented by John McQuillan.
  1985: Radia Perlman invents the Spanning Tree Protocol.
  1987: DECnet Phase V / IS-IS designed by Radia Perlman.
  2002: Beth Israel Deaconess Hospital network in Boston melts down due to deficiencies in the Spanning Tree Protocol.
  2004: TRILL presented by inventor Radia Perlman at Infocom.
  2005: TRILL presented to IEEE 802 by Radia Perlman, rejected.
  2005: TRILL presented to IETF which Charters the TRILL Working Group.
  2008: MTU problem delays protocol while fix is incorporated.

## Slide 26: TRILL in 2009/2011
  2009: RFC 5556 “TRILL: Problem and Applicability Statement”
  2009: TRILL Protocol passed up to IESG for Approval.
  2010: TRILL approved IETF Standard (2010-03-15)
    Ethertypes, Multicast addresses & NLPID assigned
  2010: Successful TRILL control plane interop at UNH IOL
  2011: TRILL Protocol base document set:
    RFC 6325: “RBridges: TRILL Base Protocol Specification”
    RFC 6326: “TRILL Use of IS-IS”
    RFC 6327: “RBridges: Adjacency”
    RFC 6361: “TRILL over PPP”
    RFC 6439: “RBridges: Appointed Forwarders”
  2011: TRILL Working Group Re-Chartered to do further development of the TRILL protocol

## Slide 27: TRILL in 2012/2013
  2012: Second Successful TRILL control plane interop at UNH IOL
  2013: Additional TRILL documents published:
    RFC 6447: FCoE (Fibre Channel over Ethernet) over TRILL
    RFC 6850: RBridge MIB
    RFC 6905: TRILL OAM Requirements
  2013: Third TRILL interop for control and data plane at UNH IOL week of May 20th
  2013: TRILL Working Group Re-Chartered to do further development of the TRILL protocol

## Slide 28: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 29: Two TRILL Examples
“Acme Power Plant” Process Control
  Large process control commonly uses Ethernet
  Some process control protocols interpret network interruption >1 second as equipment failure
  Even Rapid Spanning Tree Protocol can take >3 second to recover from root bridge failure
  Core RBridges reduce/eliminate spanning tree
“Acme Data Center”
  1:1 to N:1 Backup Improvement

## Slide 30
A
CB
CB
A = Access Bridge
GB = aGreggation
Bridge
CB = Core Bridge
GB
GB
GB
GB
A
A
A
A
A
A
A
A
A
GB
GB
A
A
A
A
A
Rapid Spanning Tree Protocol
Domain
1. Acme Power
Plant
Bridged Process Control Network
A
A
A

## Slide 31
A
CB
CB
A = Access Bridge
GB = aGreggation
Bridge
CB = Core Bridge
GB
GB
GB
GB
A
A
A
A
A
A
A
A
A
GB
GB
A
A
A
A
A
Rapid Spanning Tree Protocol
Domain
A
A
A
1. Acme Power
Plant
Spanning Tree Eliminates Loops by Disabling Ports

## Slide 32
A = Access Bridge
GB = aGreggation
Bridge
CRB = Core RBridge
RSTP
Domain
1. Acme Power
Plant
Process Control Network with RBridge Core breaking up spanning tree
RSTP
Domain
RSTP
Domain
A
GB
GB
GB
GB
A
A
A
A
A
A
A
A
A
A
A
CRB
CRB
GB
GB
A
A
A
A
A
A

## Slide 33
A = Access Bridge
GRB = aGreggation
RBridge
GRB
GRB
GRB
GRB
GRB
GRB
1. Acme Power
Plant
Process Control Network with RBridge Mesh eliminating spanning tree
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A

## Slide 34
Dist. Bridge
B
B
B
B
B
2. Acme Data Center Network with Bridges
B
B
B
B
B
B
B
B
B
B
Wan Router
Dist. Bridge
Wan Router
B = Head of Rack
Bridge
1:1 Backup
Distribution Bridges must be able to handle 100% of the load. Only 1 path available between any pair of “B”s.

## Slide 35
Dist. RBridge
H
H
H
H
H
2. Acme Data Center Network with RBridges
H
H
H
H
H
H
H
H
H
H
Wan Router
Dist. RBridge
Wan Router
Dist. RBridge
Dist. RBridge
Dist. RBridge
H = Head of Rack
RBridge
N:1 Backup
Distribution Bridges need to handle only 25% of the load. Multiple available paths between “H”s.

## Slide 36: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 37: TRILL Packet Headers
TRILL Data packets between RBridges have a local link header and TRILL Header.
  The local link header on Ethernet is addressed from the local source RBridge to the next hop RBridge for known unicast frames or to the All-RBridges multicast address for multi-destination frames.
  The TRILL Header specifies the first/ingress RBridge and either the last/egress RBridge for known unicast frames or the distribution tree for multi-destination frames.

## Slide 38: TRILL Packet Headers
Reasons for TRILL Header:
  Provides a hop count to reduce loop issues
  To hide the original source address to avoid confusing any bridges present as might happen if multi-pathing were in use
  To direct unicast frames toward the egress RBridge so that forwarding tables in transit RBridges need only be sized with the number of RBridges in the campus, not the number of end stations
  To provide a separate outer VLAN tag, when necessary, for forwarding traffic between RBridges, independent of the original VLAN of the frame

## Slide 39: TRILL Packet Headers
TRILL Header
  Nicknames – auto-configured 16-bit campus local names for RBridges
  V = Version (2 bits)
  R = Reserved (2 bits)
  M = Multi-Destination (1 bit)
  ExtLng = Length of TRILL Header Extensions
  Hop = Hop Limit (6 bits)
TRILL Ethertype
Egress RBridge Nickname
Hop
ExtLng
V
M
R
Ingress RBridge Nickname

## Slide 40: TRILL Over Ethernet
RBridge One
RBridge Two
Ethernet Cloud
DA
FCS
Payload Frame (DA, SA, VLAN/Tenant, Data)
SA
TRILL
Header
VLAN*
Ethernet Link Transport Header
Original Frame with VLAN/Tenant Label
* Link Transport VLAN only needed for VLAN sensitive link.
TRILL Ethertype 0x22F3
RBridge Three
DA
FCS
IS-IS PDU
SA
VLAN*
L2-IS-IS
Ethertype 0x22F4
Data:
IS-IS:

## Slide 41: TRILL Over PPP
PPP FCS
Payload Frame (DA, SA, VLAN/Tenant, Data)
Original Frame with VLAN/Tenant Label
PPP Link Transport Header
PPP TRILL
Data Protocol 0x005D
RBridge One
RBridge Two
PPP
TRILL
Header
PPP FCS
IS-IS PDU
PPP TRILL
IS-IS Protocol 0x405D
Data:
IS-IS:

## Slide 42: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 43: Ethernet Unicast Processing Example
Step-by-Step on Following Slides:
  Input Port Processing
  TRILL Unicast Ingress
  TRILL Unicast Transit
  TRILL Unicast Egress
  Output Port Processing

## Slide 44: Input Port Processing
Dest MAC
FCS
Data
Src MAC
VLAN
Input Native Frame on link:
Dest MAC
FCS
Data
Src MAC
VLAN
Detailed example of unicast frame TRILL routing on an Ethernet link
  Input port adds VLAN-ID and priority if frame untagged
Input Native Frame after input port:

## Slide 45: TRILL Unicast Ingress
Dest MAC
FCS
Data
Src MAC
VLAN
Input Native Frame:
1 Outer VLAN tag is a transport artifact and only needed if RBridges are connected by a bridged LAN or carrier Ethernet requiring a VLAN tag or the like.
Payload Frame
Original Frame with VLAN or Tenant ID
TRILL Header
Egress
Ingress
Ingressing
RBridge
Look Up Egress, Next Hop DA & Output Port
TTL=n
DA
New FCS
SA
VLAN1
Link Transport Header
Output TRILL Data Frame:

## Slide 46: TRILL Unicast Transit
1 Input and output Outer VLANs can differ. The true VLAN or Tenant ID of the data is inside the payload frame. Outer VLAN is only needed if link is VLAN sensitive.
Payload Frame
TRILL Hdr
Egress
Ingress
TTL=n-1
DA
FCS
Payload Frame
SA
TRILL Hdr
VLAN1
Incoming Link Transport Header
Egress
Ingress
Input TRILL Data Frame:
TTL=n
Transit RBridge
DA
New FCS
SA
VLAN1
Outgoing Link Transport Header
Output TRILL Data Frame:
Look Up Next DA & Output Port

## Slide 47: TRILL Unicast Egress
DA
FCS
Payload Frame
SA
TRILL Hdr
VLAN1
Link Transport Header
Egress
Ingress
Input TRILL Data Frame:
Egressing
RBridge
Dest MAC
Data
Src MAC
VLAN2
1 Outer VLAN only needed if RBridges are connected by a bridged LAN or carrier Ethernet requiring a VLAN tag or the like.
2 Final native frame VLAN tag may be omitted depending on RBridge output port configuration.
Output Native Frame:
New FCS
Look Up Output Port

## Slide 48: Output Port Processing
Dest MAC
Data
Src MAC
VLAN
Output Native Frame before output port:
New FCS
Output port may be configured to output untagged and will do so by default for the port VLAN ID
Dest MAC
Data
Src MAC
New FCS

## Slide 49: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 50: Fine Grained Labeling
Fine Grained Labeling (FGL) provides extended 24-bit label (or tenant ID) as the inner data label.
Ingress/egress TRILL switches that support FGL:
  Map native frame VLAN and input port into a fine grained label on ingress and
    do the reverse mapping on egress.
  Remember the priority and DEI of native frames on ingress and restores them on egress.
Fine Grained Label TRILL switches are a superset of a base protocol TRILL switches. They support VLANs as in the base standard on a port if not configured to do Fine Grained Labeling.

## Slide 51: Fine Grained Labeling
Link
Trailer
Payload Frame Data
Link
Header
TRILL
Header
Base protocol VLAN Labeling:
See:
  https://datatracker.ietf.org/doc/draft-ietf-trill-fine-labeling/
DA
SA
8100
Data Label
Pri, DEI VID
TRILL
Header
DA
SA
Link
Trailer
Payload Frame Data
Link
Header
Fine Grained Labeling:
893B
Pri, DEI Upper
893B
Pri, DEI Lower
Ingress/Egress Priority
Transit Priority
24-Bit Tenant ID
Payload

## Slide 52: Fine Grained Labeling Migration
An initial deployment of VLAN labeling TRILL switches can be smoothly extended to Fine Grained Labeling
Fine Grained Labeling TRILL Switches
FGL TR 4
FGL TR 5
FGL TR 6
FGL Labeled Path
VLAN Labeling TRILL Switches
VL TR 1
VL TR 2
VL TR 3
VLAN Labeled Path

## Slide 53: Fine Grained Labeling Migration
Some VL TRILL switches are convertible to FGL-safe RBridges (FGL transit only) with a software upgrade.
Fine Grained Labeling TRILL Switches
FGL TR 4
FGL TR 5
FGL TR 6
FGL Labeled Path
FGL TR 1
FGL TR 2
FGL TR 3
VLAN Labeled Path

## Slide 54: Fine Grained Labeling Migration
Some VL TRILL switches are convertible to FGL-safe RBridges (FGL transit only) with a software upgrade.
Even if not upgradable, they can generally be connected.
Fine Grained Labeling TRILL Switches
FGL TR 4
FGL TR 5
FGL TR 6
FGL Labeled Path
VL TR 1
VL TR 2
VL TR 3
VLAN Labeled Path
VLAN Labeling TRILL Switches

## Slide 55: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Encapsulation and Header
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 56: How TRILL Works
RBridges find each other by exchanging TRILL IS-IS Hello frames.
  Like all TRILL IS-IS frames, TRILL Hellos are sent on Ethernet to the multicast address All-IS-IS-RBridges. They are transparently forwarded by bridges, dropped by end stations including routers, and are processed (but not forwarded) by RBridges.
  TRILL Hellos are different from Layer 3 IS-IS LAN Hellos because they are small, unpadded, and support fragmentation of some information.
    Separate MTU-probe and MTU-ack IS-IS messages are available for MTU testing and determination.
  Using the information exchanged in the Hellos, the RBridges on each link elect the Designated RBridge for that link (the link could be a bridged LAN).

## Slide 57: How TRILL Works
TRILL Hellos are unpadded and a maximum of 1470 bytes long to be sure RBridges can see each other so you don’t get two Designated RBridges on the same link.
RBridge One
RBridge Two
Low MTU Dev
TRILL Cloud

## Slide 58: How TRILL Works
RBridges use the IS-IS reliable flooding protocol so that each RBridge has a copy of the global “link state” database.
  The RBridge link state includes the campus topology and link cost but also other information. Information such as VLAN/FGL connectivity, multicast listeners and multicast router attachment, claimed nickname(s), ingress-to-egress options supported, and the like.
  The link state database is sufficient for each RBridge to independently and without further messages calculate optimal point-to-point paths for known unicast frames and the same distribution trees for multi-destination frames.

## Slide 59: How TRILL Works
The Designated RBridge specifies the Appointed Forwarder for each VLAN on the link (which may be itself) and the Designated VLAN for inter-RBridge communication.
The Appointed Forwarder for VLAN-x on a link handles all native frames to/from that link in that VLAN. It is only significant if there are end station on the link.
  It encapsulates frames from the link into a TRILL Data frame. This is the ingress RBridge function.
  It decapsulates native frames destined for the link from TRILL Data frames. This is the egress RBridge function.

## Slide 60: Why Designated VLAN?
Ethernet links between RBridges have a Designated VLAN for inter-RBridge traffic. It is dictated by the Designated RBridge on the Link.
For Point-to-Point links, usually no outer VLAN tag is needed on TRILL Data frames. For links configured as P2P, there is no Designated VLAN.
However, there are cases where an outer VLAN tag with the designated VLAN ID is essential:
  Carrier Ethernet facilities on the link restrict VLAN.
  The link is actually a bridged LAN with VLAN restrictions.
  The RBridge ports are configured to restrict VLANs.

## Slide 61: How TRILL Works
TRILL Data packets that have known unicast ultimate destinations are forwarded RBridge hop by RBridge hop toward the egress RBridge.
TRILL Data packets that are multi-destination frames (broadcast, multicast, and unknown destination unicast) are forwarded on a distribution tree.

## Slide 62: Multi-Destination Traffic
Multi-destination data is sent on a bi-directional distribution tree:
  The root of a tree is a TRILL switch or a link (pseudo-node) determined by a separate election and represented by nickname.
  The ingress RBridge picks the tree, puts the tree root nickname in the “egress nickname” slot, and sets the M bit in the TRILL Header.
All the TRILL switches in a campus calculate the same trees.
All trees reach every TRILL switch in the campus.

## Slide 63: Multi-Destination Traffic
Multi-destination TRILL Data frames are more dangerous than unicast because they can multiply at fork points in the distribution tree.
  So, in addition to the Hop Count, a Reverse Path Forwarding Check is performed. This discards the frame if, for the ingress and tree, it seems to be arriving on the wrong port.
  To reduce the RPFC state, ingress RBridges can announce which tree or trees they will use.

## Slide 64: Multi-Destination Traffic
As a TRILL Data frame is propagated on a distribution tree, its distribution can be pruned by VLAN and by multicast group since it is not useful to send a frame down a tree branch if
  There are no end stations downstream in the VLAN of the frame, or
  The frame is multicast and there is no multicast listener or multicast router downstream.

## Slide 65: TRILL Nicknames
TRILL switches are identified by 6-byte IS-IS System ID and by 2-bytes nicknames.
Nicknames can be configured but by default are auto-allocated. In case of collisions, the lower priority RBridge must select a new nickname.
Nicknames:
  Saves space in headers.
  An RBridge can hold more than one nickname so that
    It can be the root of more than one different distribution tree.
    May be used to distinguish frames following traffic engineered routes versus least cost routes.

## Slide 66: Why IS-IS For TRILL?
The IS-IS (Intermediate System to Intermediate System) link state routing protocol was chosen for TRILL over OSPF (Open Shortest Path First), the only other plausible candidate, for the following reasons:
  IS-IS runs directly at Layer 2. Thus no IP addresses are needed, as they are for OSPF, and IS-IS can run with zero configuration.
  IS-IS uses a TLV (type, length, value) encoding which makes it easy to define and carry new types of data.

## Slide 67: RBridges & Access Links
You can have multiple TRILL switches on a link with one or more end stations.
The elected Designated RBridge is in charge of the link and by default handles end station traffic. But to load split, it can assign end station VLANs to other RBridges on the link.
RB1
RB2
RB3
B1
B2
B3
TRILL Cloud

## Slide 68: MAC Address Learning
By IS-IS all TRILL switches in the campus learn about and can reach each other but what about reaching end station MAC addresses?
  By default, TRILL switches at the edge (directly connected to end stations) learn attached VLAN/MAC addresses from data as bridges do.
  Optionally, MAC addresses can be passed through the control plane.
  MAC addresses can be statically configured or learned from Layer 2 registration protocols such as Wi-Fi association or 802.1X.
  Transit TRILL switches do not learn end station addresses.

## Slide 69: MAC Address Learning
Data Plane Learning
  From Locally Received Native Frames
    { VLAN, Source Address, Port }
  From Encapsulated Native Frames
    { Inner VLAN, Inner Source Address, Ingress RBridge }
    The Ingress RBridge learned is used as egress on sending
Via
  Optional End Station Address Distribution Information (ESADI) control plane protocol
  Via Layer-2 Registration protocol(s)
  By manual configuration
    { VLAN, Address, RBridge nickname }

## Slide 70: ESADI
The optional End Station Address Distribution Information (ESADI) protocol:
  Provides a VLAN/tenant scoped way for an RBridge to distribute control plane information about attached End Stations to other RBridges.
  Highly efficient transmission because information is tunneled through transit RBridges encapsulated as if it was normal data.
  Intended for use for attachment data that is either secure or that changes rapidly.
    The source RBridge selects which addresses it wants to distribute through ESADI.
    There is no particular advantage in using ESADI for large amounts of information learned from the data plane.

## Slide 71: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 72: Peering: Are TRILL Switches Bridges or Routers?
Really, they are a new species, between bridges and routers:
Routers (plus servers and other end stations)
TRILL Switches
Bridges
Hubs/Repeaters

## Slide 73: Peering
Direct Connection
Device
Device
Peers
Connection

## Slide 74: Peering
Former Situation
Router /End Station
Router /End Station
Bridge
Bridge(s)
Peers
Non-Peers

## Slide 75: Peering
Former Situation
  Or perhaps
Router /End Station
Customer Bridge
Customer Bridge
Provider Bridge(s)
Peers
Peers
Non-Peers
Customer Bridge
Provider Bridge(s)
Router /End Station

## Slide 76: Peering
Peers
Peers
Peers
With RBridges
Router /End Station
Router /End Station
TRILL Switch
TRILL Switch
Bridge(s)
TRILL Switch
Bridge(s)
Non-Peers

## Slide 77: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 78: TRILL Support of DCB
The goal is “loss-less” Ethernet. That is, no loss due to queue overflow
Basic Ethernet PAUSE “works”, but is a very blunt instrument
  Interference with loss dependent flow control such as TCP
  Blocking of high priority control frames
  Congestion spreading

## Slide 79: TRILL Support of DCB
“Data Center Ethernet”
  Priority Based Flow Control
      Per Priority PAUSE
  Enhanced Transmission Selection
  Congestion Notification
  TRILL
Data Center Bridging

## Slide 80: TRILL Support of DCB
Answer 1:
  Consider different frame priorities as different pipes
    802.1Qbb: Separate PAUSE per priority
    802.1Qaz: Ability to allocate bandwidth between these pipes
Answer 2:
  Provide back pressure on the origin of congesting flows
    802.1Qau: Congestion Notification (CN)
802.1Qbb is more commonly implemented and you would need it for surges in any case.

## Slide 81: TRILL Support of DCB
Answer 1: Consider different frame priorities as different pipes
  802.1Qbb: Separate PAUSE per priority
    Don’t enable for priorities where urgent control frames are sent or where loss dependent flow control is in use
    Enable for priorities where loss-less flow is more important.
  802.1az: Ability to allocate bandwidth between these pipes
    Highest priority frames not restricted
    Remainder of bandwidth can be carved up and frames can be selected in preference to “higher priority” frames if they have not used the allocation for their pipe.
  The above are implemented in port queuing. Can be applied to bridges, RBridges, routers, end stations.

## Slide 82: TRILL Support of DCB
For purposes of Data Center Bridging, all nodes with queues are considered peers:
Router /End Station
RBridge
Bridge
RBridge
Bridge
Peers
Peers
Peers
Router /End Station

## Slide 83: TRILL Support of DCB
Answer 2: Congestion Notification (CN): Provide back pressure on the origin of congesting flows
  When queue depth exceeds a bound, send a Congestion Notification Message CNM back to source MAC address in the congesting frame’s VLAN
  Enabled per priority. (CNM itself usually priority 6.)
  Frames can be labeled with a CN tag for more fine grained flows
  Mostly implemented in port logic
In TRILL a CN tag, if present, goes inside the encapsulated frame and a CNM is just a native frame, except for one corner case.

## Slide 84: TRILL Support of DCB
However, RBridges have to handle CNMs generated by TRILL ignorant bridges between RBridges. Such a CNM will be initially addressed to the previous hop RBridge, not the original end station.
FCS
Original Payload
TRILL Header
Link Header
Payload
Orig. DA
Orig. SA
VLAN /FGL
CN Tag

## Slide 85: TRILL Support of DCB
Previous hop RBridge has to adjust the CNM so that it goes back to the origin end station.
Note: All of the Data Center Bridging facilities depend on appropriate engineering, limited delay bandwidth product, etc., to actually provide “loss-less” service.
RBridge
RBridge
Origin
Bridge(s)
CNM
Adjusted CNM

## Slide 86: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 87: TRILL OAM
SNMP
  Used primarily to read the status and configuration of the TRILL switches but can be used to set configuration parameters.
BFD over TRILL
  Bound to TRILL port at the transmitting TRILL router. Primarily used for rapid one-hop failure detection but multi-hop supported.
TRILL OAM
  Operates between TRILL switches and is focused on testing TRILL Data paths (both fault and performance management).

## Slide 88: OAM Documents Status
SNMP
  RFC 6850, “Definitions of Managed Objects for RBridges” (MIB)
BFD over TRILL (data center)
  In RFC Editor’s queue:
    draft-ietf-trill-rbridge-bfd-07.txt
    draft-ietf-trill-rbridge-channel-08.txt
TRILL OAM (carrier grade)
  RFC 6905: TRILL OAM Requirements
  draft-ietf-trill-oam-framework-07.txt (Framework)
  draft-ietf-trill-oam-fm-00.txt (Fault Management)
  draft-ietf-trill-loss-delay-00.txt (Performance)

## Slide 89: TRILL BFD Packet Format
The BFD standard does not specify an envelope. One must be specified for each technology using BFD.
The TRILL BFD envelope uses the RBridge Channel facility, a general method for sending typed messages between TRILL routers.
Link Header
TRILL Header
TRILL Channel Header
BFD Payload
Link Trailer
Specifies BFD
Link Technology Dependent

## Slide 90: TRILL OAM Packet Format
Because TRILL OAM packets must be able to follow the same paths and get the same processing as TRILL Data packets, their format is very similar.
Link Header
TRILL Header
Truncated User Data
OAM Ethertype
OAM Channel
Link Trailer
Fixed Size
Fixed format prefix + TLVs
Link Technology Dependent
Has OAM Flag On
OAM Specific
Same as user TRILL Data except for OAM Flag

## Slide 91: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 92: TRILL Products
Announced TRILL Standard based switches:
  Broadcom – StrataXGS Trident (BMC5680)
  Cisco – Nexus
  HP/H3C – S5830V2, S5820V2
  Huawei – Cloud Engine 5800, 6800, 12800
  Mellanox – SwitchX
  Ruijie Networks – RG-S12000
  ZTE – Big Matrix 9900 Series

## Slide 93: Pre-Standard Products
“Pre-standard” products deployed
  Cisco FabricPath
    Uses TRILL control plane but different data plane
    2,000+ installations
  Brocade VCS
    Uses TRILL data plane but FSPF (Fiber Shortest Path First) control plane
    1,500+ installations

## Slide 94: TRILL Plugfests
UNH IOL TRILL interoperability event participants:
  Broadcom
  Extreme Networks
  HP/H3C Networking
  Huawei Technologies
  Ixia
  JDSU
  Oracle
  Spirent

## Slide 95: TRILL Silicon
Here are six publicly known independent silicon implementations of the TRILL Fast Path. In some cases the vendor has multiple different chips supporting TRILL.
  Broadcom – merchant silicon
  Brocade – products
  Cisco – products
  Fulcrum – merchant silicon
  Marvell – merchant silicon
  Mellanox – merchant silicon

## Slide 96: TRILL Open Source
Three Open Source Implementations
Oracle: TRILL for Solaris
  TRILL ships as part of Solaris 11
VirtuOR: www.virtuor.fr
  http://sourceforge.net/p/opentrill/wiki/Home/
TRILL Port to Linux: National University of Sciences and Technology (NUST), Islamabad, Pakistan
  Muhammad Mohsin Sardar mohsin.sardar@seecs.edu.pk
  http://wisnet.seecs.nust.edu.pk/projects/trill/index.html

## Slide 97: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 98: Comparison with MPLS
TRILL versus MPLS
  MPLS is an older, more mature technology with better Quality of Service features, etc.
  MPLS is more configuration intensive. TRILL can be auto-configuring.
  TRILL provides easier support of multicast
  TRILL can scale better because
    MPLS requires a label entry at each LSR (Label Switched Router) for each MPLS path through that LSR
    TRILL requires a nickname entry at each RBridge for each TRILL switch in the campus

## Slide 99: Comparison with IP
TRILL versus IP
  IP is an older, more mature technology
  TRILL supports VM mobility. Changing subnets changes IP Address, breaking TCP connections
  TRILL is better at multicast because
    IP requires a complex protocols like PIM to do multicast
    TRILL has simple multicast distribution, with pruning for optimization, designed in from the start

## Slide 100: Comparison with 802.1aq
SPB is IEEE 802.1aq, “Shortest Path Bridging”, a project of the IEEE 802.1 Working Group, which was approved as an IEEE standard near the end of March 2012.

## Slide 101: Comparison with 801.1aq
Similarities:
  Both provide shortest path forwarding.
  Both use IS-IS
    TRILL has always used true IS-IS routing.
    SPB started using many spanning trees and then switched to using IS-IS to configure bridge forwarding.
  Both require end station address learning only at the edge. Transit switches do not learn end station addresses.

## Slide 102: Frame Overhead Details
For point-to-point links with multi-pathing:
  TRILL:
    20 bytes for Ethernet (+ 8 TRILL Header (including Ethertype) + 12 outer MAC addresses)
    8 bytes for PPP
  SPBM:
    22 bytes for Ethernet (+ 18 802.1ah tag – 12 for MAC addresses inside 802.1ah + 4 B-VLAN + 12 outer MAC addresses)
    24 bytes for Ethernet over PPP, native PPP not supported
For complex multi-access links with multi-pathing:
  TRILL: 24 bytes (20 + 4 for outer VLAN tag)
  SPBM: multi-access links not supported

## Slide 103: Routing Computation
N = number of switches k = number of multi-paths
IETF TRILL Standard
  For unicast frames, N×log(N).
    Arbitrary multi-pathing available by just keeping track of equal cost paths.
  For multi-destination frames, k×N×log(N) to have k distribution trees available.
IEEE Std 802.1aq
  Unicast and multi-destination unified: k×N2×log(N) for k-way multi-pathing.
  Planned to be improved by 802.1Qbp project.

## Slide 104: Comparison with 801.1aq
OAM
  SPB: Currently supports IEEE 802.1ag (Continuity Fault Management, CFM).
  TRILL: Supports IETF BFD (Bidirectional Forwarding Detection) protocol and carrier-grade OAM similar to CFM being developed
Data Label Granularity
  SPB: Supports 4K VLANs or 2**24 Service Identifiers.
  TRILL: Supports 4K VLANs and 2**24 Fine Grained Labels.

## Slide 105: Comparison with 801.1aq
Peering:
  RBridges peer through intervening bridges.
  SPB bridges must be directly connected and only peer within a contiguous SPB region.
Spanning Tree:
  TRILL RBridges block spanning tree and provide a new level above bridging but below Layer 3 routing.
  SPB bridges run at the bridging level. They continue to maintain a spanning tree (or multiple spanning trees) hooking together any attached bridging to produce one huge spanning tree. Frames are forwarded by spanning tree or by shortest path depending on VLAN.

## Slide 106: Comparison with 801.1aq
B
B
B
B
B
B
B
B
B
B
B
B
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
B = core Bridge
EB = edge Bridge – where many end stations are connected
Yellow = Ordinary Bridging

## Slide 107: Comparison with 801.1aq
B
B
B
B
B
B
B
B
B
B
B
B
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
One spanning tree
(there could be multiple)

## Slide 108: Comparison with 801.1aq
S
B
S
B
S
S
S
S
S
B
B
B
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
S = Shortest Path Bridge
Orange = SPB Region
Spanning Tree Penetrates SPB Regions

## Slide 109: Comparison with 801.1aq
R
B
R
B
R
R
R
R
R
B
B
B
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
EB
R = RBridge (TRILL switch)
Spanning Tree terminated by RBridges

## Slide 110: CONTENTS
What is TRILL?
TRILL Features
TRILL History
Two TRILL Examples
TRILL Packet Headers
Step-by-Step Processing Example
Fine Grained Labeling
How TRILL Works
Peering and Layers
TRILL Support of DCB
TRILL OAM
TRILL Products
Comparisons
Standardization and References

## Slide 111: Standardization Status
The TRILL protocol RFCs (bold = stds track)
  RFC 5556, “TRILL Problem and Applicability”
  RFC 6325, “RBridges: TRILL Base Protocol Specification”
  RFC 6326, “TRILL Use of IS-IS”
  RFC 6327, “RBridges: Adjacency”
  RFC 6361, “TRILL over PPP”
  RFC 6439, “RBridges: Appointed Forwarders”
  RFC 6847, “FCoE over TRILL”
  RFC 6850, “Definitions of Managed Objects for RBridges” (MIB)
  RFC 6905, “TRILL OAM Requirements”

## Slide 112: Standardization Status
  Document that are fully approved and in the RFC Editor’s Queue. These are expected to issue as standards track RFCs soon:
    “TRILL: Fine Grained Labeling:
      https://datatracker.ietf.org/doc/draft-ietf-trill-fine-labeling/
    “TRILL: BFD Support”
      https://datatracker.ietf.org/doc/draft-ietf-trill-rbridge-bfd/
    “TRILL: RBridge Channel Support”
      https://datatracker.ietf.org/doc/draft-ietf-trill-rbridge-channel/
    “TRILL: Edge Directory Assistance Framework”
      https://datatracker.ietf.org/doc/draft-ietf-trill-directory-framework/
    “TRILL: Clarifications, Corrections, and Updates”
      https://datatracker.ietf.org/doc/draft-ietf-trill-clear-correct/
    “TRILL: Header Extension”
      https://datatracker.ietf.org/doc/draft-ietf-trill-rbridge-extension/

## Slide 113: Standardization Status
Non-IETF Assignments:
  Ethertypes assigned by IEEE:
    TRILL Data: 0x22F3
    TRILL IS-IS: 0x22F4
    TRILL Fine Grained Labeling: 0x893B
    RBridge Channel: 0x8946
  Block of multicast addresses assigned to TRILL by IEEE:
    01-80-C2-00-00-40 to 01-80-C2-00-00-4F
  TRILL NLPID (Network Layer Protocol ID) assigned from ISO/IEC: 0xC0

## Slide 114: More TRILL References
TRILL Introductory Internet Protocol Journal Article:
  http://www.cisco.com/web/about/ac123/ac147/archived_issues/ipj_14-3/143_trill.html
The first paper: Perlman, Radia. “Rbridges: Transparent Routing”, Proceeding Infocom 2004, March 2004.
  http://www.ieee-infocom.org/2004/Papers/26_1.PDF

## Slide 115: Some TRILL Futures
Carrier grade OAM
Directory Assisted Edge:
    In data centers, the location of all MAC and IP address and virtual machines is typically known through orchestration. This information can be provided to edge TRILL switches by a directory.
    Directory information can be Pushed or Pulled and can reduce or eliminate ARP (IPv4), ND (IPv6), and unknown unicast MAC flooding.
Active-active at the edge
Multi-level and Multi-topology support

## Slide 116: END
Donald E. Eastlake 3rd
Co-Chair, TRILL Working Group
Principal Engineer, Huawei
d3e3e3@gmail.com

## Slide 117: Backup Slides
Donald E. Eastlake 3rd
Co-Chair, TRILL Working Group
Principal Engineer, Huawei
d3e3e3@gmail.com

## Slide 118: Algorhyme (Spanning Tree)
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
Is loop-free connectivity.
A tree that must be sure to span
So packets can reach every LAN.
First, the root must be selected.
By ID, it is elected.
Least-cost paths from root are traced.
In the tree, these paths are placed.
A mesh is made by folks like me,
Then bridges find a spanning tree.
- By Radia Perlman

## Slide 119: Structure of an RBridge
Central Processing IS-IS, Mgmt., Etc.
Switching fabric
Port Logic
Port Logic
Port Logic
Port Logic
Links to other devices. Could be 802.3 (Ethernet), 802.11 (Wi-Fi), PPP, …

## Slide 120: Structure of an RBridge Port
Assumes an Ethernet (802.3) link.
Information
Frame & Info
802.3 Physical Interface
802.3 Link
802.1/802.3 Low Level Control Frame Processing, Port/Link Control Logic
802.1Q Port VLAN Processing
RBridge: High Level Control Frame Processing (BPDU, VRP)
ISS
RBridge: Higher Level Processing (see next slide)

## Slide 121: Structure of an RBridge Port
Information
Frame & Info
Lower Level Processing (see previous slide)
RBridge: Inter-port Forwarding, IS-IS, Management, Etc.
Appointed Forwarder and Inhibition Logic
Native frames
Encapsulation / Decapsulation Processing
TRILL IS-IS Hellos
TRILL IS-IS Hello Processing
TRILL Data
Other TRILL IS-IS
TRILL Data

## Slide 122: Loop Avoidance
All possible forms of looping behavior within a TRILL campus can be grouped into one of three classes:
  TRILL Data Packet Loops, in which the packet would remain TRILL encapsulated.
  Hybrid TRILL Data / Native Frame Loops, in which the frame is repeatedly encapsulated and decapsulated.
  Native Frame Loops, in which the frame is never encapsulated.
    Since TRILL always encapsulates data, if you have this problem, no RBridges are involved so it is not TRILL’s fault.

## Slide 123: Loop Avoidance
TRILL Data Packet Loops:
  Known unicast TRILL Data packets have a hop count and are always unicast to the next hop RBridge towards their destination.
  Multi-destination TRILL Data packets must be received on a port which is part of their distribution tree, the ingress RBridge nickname and input port must pass a Reverse Path Forwarding Check, and they have a hop count.

## Slide 124: Loop Avoidance
Hybrid TRILL Data / Native Frame Loops:
  Such a loop would require, at some point around the loop, that a TRILL Data packet be decapsulated onto a link by one RBridge and then picked up and re-encapsulated by another RBridge.
  TRILL takes great care to minimize the probability of there being two uninhibited appointed forwarders on the same link for the same VLAN.
    Under certain conditions, an RBridge appointed forwarder is inhibited from accepting or sending native frames. This only affects native frames. An RBridge port is never inhibited or blocked from sending or receiving TRILL Data or TRILL IS-IS frames except by very low level link flow control mechanisms such as PAUSE or if the port has been manually configured as disabled.

## Slide 125: What About Re-Ordering?
RBridges are required to maintain frame ordering internally, modulo flow categorization.
When multi-pathing is used, all frames for an order-dependent flow must be sent on the same path if unicast or the same distribution tree if multi-destination.
Unicast re-ordering can occur briefly when a destination address transitions between being known and unknown, or a topology change occurs.
  This can be minimized with keep-alives, ESADI, distribution tree per RBridge, or configured addresses.

## Slide 126: PDU Types
PDU Type Names Used in TRILL
  TRILL Packets
    TRILL IS-IS Packets– Used for routing control between RBridges.
    TRILL Data Packets– Used for encapsulated native frames.
  Layer 2 Control Frames – Bridging control, LLDP, LACP, etc. Never forwarded by RBridges.
  Native Frames – All frames that are not TRILL or Layer 2 Control Frames.

## Slide 127: PDU Types, More Detail
TRILL Packets– Ethernet local link encoding
  TRILL Data packets – Have the TRILL Ethertype and are sent to a unicast address or, if multi-destination, to the All-RBridges multicast address.
  TRILL IS-IS Packets – Have the L2-IS-IS Ethertype and are sent to the All-IS-IS-RBridges multicast address.
  (TRILL Other packets– sent to a TRILL multicast address but not a TRILL Data or TRILL IS-IS frame. Not currently used.)

## Slide 128: PDU Types, More Detail
Layer 2 Control Frames – Destination Address is 01-80-C2-00-00-00 to 01-80-C2-00-00-0F or 01-80-C2-00-00-21
  High Level – BPDU (01-80-C2-00-00-00) & VLAN Registration (01-80-C2-00-00-21)
    RBridges handle these differently from bridges. The spanning tree protocol never runs through an RBridge but an RBridge port is not prohibited from participating in spanning tree as a leaf node.
  Low Level – all other control frames
    An RBridge port may implement other Layer 2 protocols such as LLDP (Link Layer Discovery Protocol), 802.1AX (Link Aggregation), 802.1X (Port Based Access Control), 802.1AE (MAC Security), and the like.