## Slide 1
IPv6-only?
You’re kidding, right?
Lee Howard, Wes George
{lee.howard,wes.george}@twcable.com

## Slide 2: Test Environment/OS Notes
Cable Modem filtering IPv4, directly connected to the host under test
Host receives IPv6 prefix and IPv6 DNS via DHCPv6
Windows (7/8) – Works
Mac OS (10.7+) – Works
Ubuntu (13.04) – Works
Not tested – Wi-Fi connected devices behind a GW is next phase of testing
Android – no DHCPv6 support
  https://code.google.com/p/android/issues/detail?id=32621
    filed in 2012, Medium priority enhancement, no owner
iOS – sorta works
  Some testing details available from Andrew Yourtchenko’s RIPE66 talk
    here: https://ripe66.ripe.net/archives/video/1196/
Notes: Fundamental to any further testing of an end user’s experience – how does the OS’s networking stack handle an IPv6-only network?
Good news is that the major desktop OSes just work – no hacks or other hand-holding required. Important thing here is to make sure that it works without any configuration changes away from the defaults (remember, average user…)
Android also has limited (or no) UI to configure IPv6 addresses, DNS, etc.
If any of you want to hack on the Android network stack, it appears they could use a volunteer to implement this enhancement
The talk referenced links to a bug opened on iOS where apps are often using an IPv4-only connectivity check, and when that fails, they assume they have no network connectivity
Ok, now with the OS sorted, what happens with content?

## Slide 3: What happens when all you have is IPv6?
Let’s turn off IPv4 and find out…
Notes: We know that dual-stack isn’t a useful end state, because it requires us to keep running IPv4 (or more than likely, some crappy substitute with umpteen layers of NAT) indefinitely. We wondered where we were in relation to the point where an internet user – any internet user – could go IPv6-only and have their daily activities work properly.
Short answer is that we’re not there yet, but we did learn a lot of interesting things.

## Slide 4: It just works!
WIN

## Slide 5: … for some values of “work”
Notes: We’ve found that a lot of sites are only partially IPv6-capable. CSS, images, subdomains, download sites/CDNs, etc are often pulled from a different IPv4-only server. So you end up with sites transported back to 1997/web 1.0 when their CSS doesn’t load, some unaccessible content, and often NO ADS! (feature?)
Best example – one Unix distro (remaining nameless) uses some sort of algorithm to choose the best download mirror. It displays your IP (so it shows I had an IPv6 address) and then redirected to an IPv4-only mirror – took multiple reloads before it finally found an IPv6-enabled mirror.

## Slide 6: Except… when it doesn’t
FAIL
Notes: Yes, it’s bad form to call out other people’s mistakes on enabling their sites for IPv6 without acknowledging that ours currently doesn’t work at all. We’re not happy about it either.
But this is a good learning experience to be had at our expense – sometimes the folks who worked on the initial effort to enable the site for IPv6 move on, and don’t tell their replacements they had turned on IPv6, and when the site migrates to a new home, the IPv6 connectivity goes away, and there’s nothing in the monitoring system screaming at them to let them know they broke it. This is why it is so important to ensure that your tools and monitoring and processes and documentation treat IPv6 as production.

## Slide 7: Test results – Do webpages work over IPv6-only?
World IPv6 Launch Participants
(random sample, mainly US/CA)
Chart: 
| Yes | Mostly | Sorta | No
 | 133 | 25 | 23 | 60
Other sites
Chart: 
| Yes | Mostly | Sorta | No
 | 11 | 2 | 2 | 37
Notes: It’s fairly obvious that IPv4-only sites aren’t going to work over IPv6. So what about the sites that are supposedly IPv6-capable? We did a little bit of random sampling of the WVL participants, mostly the top Alexa ranked sites from the US and Canada, along with a random sampling of others
“Other sites” were a cross-section of tech sites, vendors, other things that were personally interesting to the tester, but were not listed as WVL participants
Yes: No issues detected
Mostly: some non-critical content doesn't load (ads, a few images, 1 subdomain link fails out of many that work, etc)
Sorta: part of the page loads, but is missing major elements (CSS, all/most images) or the main page is IPv6-enabled, but most/all subtending links fail
No: unable to reach this page via IPv6 or page fails to load enough for even basic use (eg only top nav bar loads)

## Slide 8: A little experiment with our favorite sponsors. . .
Host
Platinum Sponsor
Gold Sponsor
Silver Sponsors
Supporting Sponsor

## Slide 9: A little experiment with our favorite sponsors. . .
Host
Platinum Sponsor
Gold Sponsor
Silver Sponsors
Supporting Sponsor
WIN
FAIL
Sorta
WIN
WIN
FAIL
FAIL
FAIL

## Slide 10: So what?
Those with IPv6 websites and apps need to start testing them with IPv4 disabled
  Dual-stack (especially with Happy Eyeballs) masks problems with your IPv6 connectivity
Monitor your IPv6 site just like you monitor your IPv4 site
  Can’t fix what you don’t know is broken
  An IPv6 outage should have the same urgency and impact as an IPv4 outage
  Again, single-stack IPv6 is better at exposing problems
Those without IPv6 enabled on their websites…

## Slide 11: How committed is your company to IPv6?
IPv6
“IPv6 is important…”
“We’re committed to IPv6…”
“We are your IPv6 partner…”
Your Logo here
Time to make that commitment publicly visible:
Turn on IPv6 on all of your external services
Notes: “how can we trust you to know what you’re doing with IPv6 on our network, if you can’t/won’t/don’t find it important to enable it on your own website?”
“IPv4 costs us money (we’ve shown why in previous presos), why would I buy your gear if you’re costing me money?”