## Slide 1: Over coming traditional network limitations with open source

## Slide 2
Modern datacenters adoption of new technologies
application demands push protocol scale
physical (100Gbps distance, speed of light)
administrative (layer 8) resources
“SDN”, OpenFlow, network virtualization, configuration management, and many other efforts are throwing a wrench against traditional networking practices
October 16, 2013
<number>

## Slide 3: Traditional networking
Typical Network Operating System (switch and/or router)
Structured as “black box”
  CLI != API
Closed development model
  Diagnostics “under the hood” difficult to see
Complicated management tool chains
  SNMP MIB’s… hell
  Screen scraping… regex’s change on OS version
  Arcane / low adoption scripting languages
Not geared for rapid spin-up / spin-down of resources
October 16, 2013
<number>

## Slide 4: Modern datacenter network roots
IP-based networks
  Limited adoption - large scale L2, InfiniBand, ATM
Configuration management / automation
  Monitoring
  Policy enforcement
  Rapid spin-up / spin-down
New breed of applications
  East-West vs. North-South flows
October 16, 2013
<number>

## Slide 5: Linux?
Dominate server platform
  Well established ecosystem of distributions, best practices, knowledge
  Open well documented API, large selection of language interpreters
  Excellent networking support - IPv6, NAT’s, QoS, accounting
Vibrant community which fuels rapid innovation
Heavy automation frameworks
  Open nature has facilitated huge management tool-chain progress
October 16, 2013
<number>

## Slide 6: In other words…
  GNU/Linux is a great fit as the OS for not just servers but also routers and switches in the modern data center
October 16, 2013
<number>

## Slide 7: Operating System Evolution
October 16, 2013
<number>
Linux as the embedded OS: process and memory mgmt
Embedded OS with process and memory mgmt
No real OS, while loop
Monolithic OS
3rd Real-time OS
Linux-based OS
Eg: IOS, CatOS
Proprietary routing
And switching stack
Eg: ION
Eg: NX-OS, EOS
Cumulus Linux
Linux OS
Linux as
Network OS:
Native routing
and switching
Proprietary routing
And switching stack
Proprietary routing
And switching stack

## Slide 8
What advantages does this provide?
October 16, 2013
<number>

## Slide 9: Open Source L2 & L3
Routing
  Quagga (many forks), BIRD, Xorp
    OSPF unnumbered
    Looking glass
Bridging
  Kernel STP, MSTPD (BDPU Guard, Bridge Assurance)
Discovery
  LLDAP, Open-LLDP, LLDPD (many implement CDP, FDP, etc.)
October 16, 2013
<number>

## Slide 10: L8 Management
Traditional tools
  TCL – limited adoption
  XSLT – single vendor, mostly supplied tools
  Except – Rancid base, very popular
“DevOps” tools have major adoption
  Cfengine, Puppet, Chef, Ansible
  Salt, Trigger, … literally new tools every quarter
  Large diverse communities (conferences, books, professional services)
  Nirvana = same tool chain for compute AND network environments
“NetDevOps” re-born again
  NetDev abstraction layer in puppet, chef, & ansible
  Possible “SDN” pill which CCIE’s can appreciate?
October 16, 2013
<number>

## Slide 11: Monitoring
Traditional tools
  SNMP – Where can I get a copy of the MIB?
  MRTG
  Cacti
Newer tools (again, compute folks learned long ago SNMP was a fail)
  CollectD
  Diamond
  Graphite
  Sensu
Deploy agents directly on the network devices, pushing stats and state, instead of polling
October 16, 2013
<number>

## Slide 12: Cumulus Networks contributions
ONIE
  Open Source boot loader for network devices
Prescriptive Topology Daemon
  Data centre cable verification using LLDP
Quagga
  Actively submitting patches, major bugfixes
MSTP
  Bridge assurance, various bugfixes
October 16, 2013
<number>

## Slide 13: ONIE - Open Network Install Environment
Problem:
Switches need the equivalent of a boot loader to allow disaggregation of hardware from operating system
Solution: ONIE, installer environment to address open hardware ecosystem
A small, Linux based operating system that comes pre-installed on bare metal switches
Provides an environment for network OS installers (Network operating system neutral)
October 16, 2013
<number>
Bare metal switch
operating system
app
app
app
ONIE
Bare metal server
operating system
app
app
app
BIOS
Server
Switch

## Slide 14: ONIE - Open Network Install Environment
Zero-touch install of operating system on industry-standard gear running the Open Network Install Environment (ONIE)
  Industry standard gear comes with ONIE
  ONIE provides the installer environment for auto-installation of network operating system
  ONIE discovers the operating system through USB, DHCP,..., and Cumulus Linux gets downloaded and installed on the system
1- Discover installer on management interface:
USB, URL from DHCP, URL from DNS-SD, ….
2- Download, run installer, and reboot
onie-installer
October 16, 2013
<number>

## Slide 15: Prescriptive Topology Module
Topology graph:
  Graph G {
      S1:p1 – M1:p3;
      S1:p2 – M2:p3;
      S1:p3 – M3:p3;
      S1:p4 – M4:p3;
      S2:p1 – M1:p4;
      S2:p2 – M2:p4;
      S2:p3 – M3:p4;
      S2:p4 – M4:p4;
      M1:p1 – T1:p1;
      M1:p2 – T2:p2;
      …
      M4:p2 – T4:p2;
    }
Goal: Operational simplicity, reduced Operator errors
  Verify connectivity per cabling plan
  Bring up routing adjacency only if cabling test passes
  Selective actions on link up
How? Network topology specified via DOT language and distributed to all nodes
  Each node determines its relevant information
  Use LLDP to verify connectivity
  Logs errors
  Daemon executes a set of scripts on topology pass and a different set of scripts on topology fail
Topology
S2
M2
M1
T2
T1
M4
M3
T4
T3
S1
October 16, 2013
<number>

## Slide 16: Prescriptive Topology Module
Topology
s1
s0
l1
l0
October 16, 2013
<number>
digraph G {
//spine0's connections
spine0:swp1 -> leaf0:swp1;
spine0:swp2 -> leaf1:swp1;
//spine1's connections
spine1:swp1 -> leaf0:swp2;
spine1:swp2 -> leaf1:swp2;
//leaf0's connections
leaf0:swp1 -> spine0:swp1;
leaf0:swp2 -> spine1:swp1;
//leaf1's connections
leaf1:swp1 -> spine0:swp2;
leaf1:swp2 -> spine1:swp2;
}

## Slide 17: Prescriptive Topology Module
October 16, 2013
<number>
cumulus@S1:~# ptmctl
---------------------------------------------------------------------
Port Status Expected Nbr Observed Nbr Last Updated
---------------------------------------------------------------------
swp1 pass M1:swp3 M1:swp3 17h:39m:21s
swp2 pass M2:swp3 M2:swp3 17h:39m:21s
swp3 pass M3:swp3 M3:swp3 17h:39m:21s
swp4 pass M4:swp3 M4:swp3 17h:39m:21s
Swp5 fail M5:swp3 M4:swp4 17h:39m:21s
cumulus@S1:~#
Written in C and Python
Communicates with LLDPD (based on https://github.com/vincentbernat/lldpd)

## Slide 18: Prescriptive Topology Module
October 16, 2013
<number>
Interoperability
Any device running an LLDP daemon
Routing adjacencies can be brought by the device running PTM.
digraph G {;
S1:swp1 -> S2:swp1;
S1:swp2 -> S2:swp2;
S1:swp3 -> "procurve1.lab":21;
S1:swp4 -> "procurve1.lab":22;
S1:swp5 -> "cisco1.lab":"GigabitEthernet0/1";
S1:swp6 -> "jmx480":"xe-0/0/0";
S1:swp7 -> webserver1:eth0;
S1:swp8 -> webserver1:eth1;
}
cumulus@S1:~# ptmctl
---------------------------------------------------------------------
Port Status Expected Nbr Observed Nbr Last Updated
---------------------------------------------------------------------
swp1 pass S2:swp1 S2:swp1 17m: 2s
swp2 pass S2:swp2 S2:swp2 17m: 2s
swp3 pass procurve1.lab:21 procurve1.lab:21 17m: 10s
swp4 pass procurve1.lab:22 procurve1.lab:22 17m: 10s
swp5 pass cisco1.lab:GigabitEthernet0/1 cisco1lab:GigabitEthernet0/1
swp6 pass jmx480.lab:xe-0/0/0 jmx480.lab:xe-0/0/0 17m: 1s
swp7 pass webserver1:eth0 webserver1:eth0 17m: 3s
swp8 pass webserver1:eth1 webserver1:eth1 17m: 3s

## Slide 19
What are we missing?
Hardware acceleration of the networking forwarding path
October 16, 2013
<number>

## Slide 20: One way of hardware accelerating
October 16, 2013
<number>

## Slide 21: Thank you!
nat@cumulusnetworks.com | @natmorris
Notes: Also twitter “@
<number>