## Slide 1: Reducing the impact of IXP maintenance
Will Hargrave // LONAP
will@lonap.net

## Slide 2: What is an IXP?
A switched fabric for interconnecting networks
BGP is the control plane for network operators to signal reachability
What happens to production traffic when an IXP operator does maintenance?

## Slide 3
ISP router A
IXP Switches
192.0.1.2
192.0.1.3
A typical IXP
BGP Session
ISP router B

## Slide 4
ISP router A
ISP router B
IXP Switches
192.0.1.2
192.0.1.3
Maintenance
BGP Session

## Slide 5
192.0.1.2
192.0.1.3
Waiting for BGP holdtimers…
BGP Session
Where’s my peer?
Where’s my peer?
Traffic blackholed here 
ISP router A
ISP router B

## Slide 6
IXP Switches
192.0.1.2
192.0.1.3
90 to 180 seconds later….
BGP Session
Holdtimer expired
Holdtimer expired
ISP router A
ISP router B

## Slide 7: Improving the experience
In many cases, IXP switch maintenance causes 90seconds+ blackholing of production traffic
We are doing things the wrong way round!
Solution:
  At the start of the maintenance window, tear down the control plane!
  Wait for traffic to diminish (3-5 minutes)
  Now do your maintenance
How to tear down the control plane? Answer: L4 ACLs on IXP port!

## Slide 8: L4 ACLs on IXP
entry DenyBGPv4e {
if {
source-address 5.57.80.0/22;
protocol tcp;
source-port 179;
} then {
deny;
}
}
entry DenyBGPv4i {
if {
source-address 5.57.80.0/22;
protocol tcp;
destination-port 179;
} then {
deny;
}
}
entry DenyBGPv6e {
Your IXP subnet
Block in both directions, otherwise sessions will re-establish
Obviously repeat this for IPv6 too

## Slide 9: End
We tested this during two recent LONAP maintenances with success.
Questions? Comments?
Will Hargrave
will@lonap.net